## Slide 1
H9FECC · Fog and Edge Computing · CA Project
Smart City Pollution Monitor
Fog-enabled AQI analytics with a serverless AWS backend
PRESENTER
Pavan
MSc in Cloud Computing, NCI
FIVE POLLUTANTS
PM₂.₅ · PM₁₀ · NO₂ · CO · O₃

## Slide 2
Why this matters
Urban air quality varies block by block — a cloud-only design is both slow and wasteful.
60 %
Reduction in bytes shipped to cloud when AQI is computed at the edge.
2 s
Local dashboard update via Server-Sent Events.
0
Sensor readings dropped under injected DynamoDB throttling.
Moving analytics to the fog layer is the dominant design lever.

## Slide 3
Architecture
SENSOR LAYER
PM₂.₅
PM₁₀
NO₂
CO
O₃
FOG NODE
Flask ingest
/sensor-data
Rolling deque
size=20 per sensor
AQI compute
EPA breakpoints
Z-score flag
κ=2.5
Dispatch
batched POST
CLOUD LAYER (AWS)
API Gateway
Lambda: IngestToQueue
Amazon SQS
Lambda: ProcessQueueToDB
Amazon DynamoDB
S3 dashboard + SSE stream

## Slide 4
Edge analytics: AQI + Z-score
AQI (US-EPA breakpoint)
I = (I_hi - I_lo) / (C_hi - C_lo)
* (C - C_lo) + I_lo
• Linear interpolation between concentration breakpoints.
• Category labels: Good → Moderate → Unhealthy → Hazardous.
• Per-sensor breakpoint tables (PM, NO₂, CO, O₃).
• Computed at the fog layer — no cloud round-trip needed.
Anomaly (rolling Z-score)
|x - mu| > k * sigma, k = 2.5
• Rolling deque size W = 20 per sensor.
• μ, σ computed on the fly each tick.
• κ configurable per pollutant — avoids false positives in rush hour.
• Flag attached to payload before cloud dispatch.

## Slide 5
Smart city dashboard
Live AQI by pollutant, category chips, and five Chart.js lines.

## Slide 6
Sensor simulator running
AQI labelling
Each reading tagged Good / Moderate / Unhealthy / Hazardous.
Realistic dynamics
Gaussian noise + rush-hour peaks + rare spikes.
Own cadences
Five threads, five dispatch intervals.

## Slide 7
Fog node dispatch + retry
Batches of 5
5 processed readings per dispatch.
Retry semantics
3 retries on 202 / 5xx before dropping.
Back-pressure
Warnings logged when backend is slow.

## Slide 8
Scalable serverless backend
Competing consumers
SQS decouples ingest and storage; Lambda scales with message rate.
PAY_PER_REQUEST
DynamoDB auto-scales read/write units; zero idle cost.
SSE over polling
Push real-time updates to the dashboard with one line of JS.
IAM least privilege
Per-Lambda roles: SQS-only, Dynamo-only, read-only.

## Slide 9
Results
< 2 s
SSE local latency
< 4 s
Cloud polled latency
100 %
delivery via retries
$0.28
monthly AWS cost
Headline
Edge analytics cut bandwidth and latency; serverless scale-out handles load with zero ops.

## Slide 10
Hardest problem → my fix
Challenge
• Rush-hour peaks looked like anomalies.
• Too low κ → false positives; too high → missed spikes.
• Intermittent backend → retries needed care.
Fix
• κ is a per-sensor config setting, not a global constant.
• Fold time-of-day factor into the baseline before Z-score.
• Exponential back-off + 3-try dispatch with structured logs.
• SQS + DynamoDB retry catches the rest.

## Slide 11
Thank you.
Questions · live demo
Pavan · H9FECC · NCI MSc Cloud Computing